## Slide 1: Binvox creation + Segmentation
Jan

## Slide 2: .STL to .binvox
Max .binvox dim is 512x512x512 = squeezing everything into 512 voxels
Loss of resolution if a feature is less than 1/512 of max length
  Otherwise increase of resolution
How to increase .binvox dim?
  Crack binvox.exe / decompile – not a good idea / 99 $ (max 4200 voxels)
  Segment STL into parts – then 512 binvox
    Deleting vertices ?
    Complicated , idk

## Slide 3: Solution: Create binvox with python!
TIME-INTENSIVE but POSSIBLE!!! (memory problems ? )
Any part can be voxelized
.Stl file in bounding box (x and y stay parallel)  Orientation matters
X
y
Turning alg. Necessary !!!

## Slide 4: Segmentation
HD picture from HD binvox
Subdivide into 64x64 pix with overlap
Subdivide into 128x128 pix with overlap – resize to 64
Subdivide into 256x256 pix with overlap - resize to 64
……

## Slide 5: Results

## Slide 6: Loop for precise location
Take all pictures
Find all features and position
Draw all BB on HD picture
If feature is found on 2 or more dimensioned pictures assume its true
Remove predictions with less then 99%
Remove predictions that occur only in 1 dimensioned picture set

## Slide 7: How To Turn a .Stl – minimizing BB

## Slide 8: The big question
How to locate a feature on a slope ?
localization possible if surface in line with axes – how to turn ?

## Slide 9: Problem and solution
picture from binvox that is not a cube
  Dimensions not equal
  Reading problem in high dimensions ????
WHY BINVOX AT ALL ??????
  Pickledump everything !!!!!

## Slide 10: Problem
If feature-depth is small compared to total depth:
  Difficult to see (human) on .png

## Slide 11: NEW 5.8.2021

## Slide 12: New VOXELIZER
Create png-s
Remove bars
combine
X
y
Turning alg. Necessary !!!

## Slide 13: The big question
How to locate a feature on a slope ?
localization possible if surface in line with axes – how to turn ?
Has to be done PRE-voxelisation

## Slide 14: Turning
Take all normal of all planes
Add areas of normal that point in the same direction
Sort by area
Turn file so normal are parallel to axes
Voxelize

## Slide 15: Result of turning
How to combine recognized features
Ascii VS binary
Have Z values of planes to turn back and assign to original stl

## Slide 16: NEW 11.8.2021

## Slide 17: How to glue everything together
BIG FLOWCHART NEEDED (TO DO)

## Slide 18: Turning – problem = Size not constant

## Slide 19: Turning – problem = Where is it placed ?
At top ?
At bottom ?
At centre ?
Position needed – for Z direction
Angle needed - for turning
relative size change needed – for scaling
X
X
X*(2)**0.5
X2+x2 = c2  c= q2 (2 x2) = x* q2 (2) f = c/x = q2(2)
a
A*squ(2)
X2 min max
Y2 min, max
L
orig

## Slide 20: Turning – problem = Size not constant
Get
xmin, xmax
Yin,ymax
IS POSSIBLE

## Slide 21: Small achievements 
Solved Deprecated version problem
Updated all libs to newest version

## Slide 22: IDEAS
Time optimization ???
Small scale test to validate results
DO NOT CHANGE ALL .CPU TO. GPU !!!
Creating HD pictures takes the longest time ??????
Sometimes pushing to GPU is not recommended because not enough memory – ram better

## Slide 23: Questions
End result
Grant extension